## Slide 1: CPO
2025/09
Co-packaged Optics

## Slide 2: Table of contents
Lorem ipsum dolor
Lorem ipsum dolor
01. Why the Focus on CPO?
02. Why Copper to Optical? Why Pluggable to Co-packaged?
03. Where CPO Fits First: Scale-up or Scale-out?
04. How Big is the CPO Market?
05. Which Segment Matters Most?
Lorem ipsum
Lorem ipsum
06. Key Players to Watch: Broadcom and FiconTEC
Tech
Interconnect
Optical
CPO
Markets
Sizing
Segments
Players

## Slide 3: Why the Focus on CPO? Nvidia, Broadcom, and DeepSeek
IMAGE
Pivots from Copper to Optics
Launches 2 CPO Switches
Premieres advanced CPO switches
GTC 2025
IMAGE
Bandwidth limitation restricts training, inference, and network strategies
CPO: higher bandwidth & energy efficiency
《Insights into DS-V3》
CPO matters under limited bandwidth in China
IMAGE
TH4: 1st CPO switch chip
TH6: fastest CPO switch chip, announced in April
Tomahawk Switches
Accelerates CPO ecosystem adoption

## Slide 4
Speed
Low power + extended distance requires reduced data rates or bandwidth
1
Power
Long-distance suffers signal attenuation, requiring power compensation
3
Communication Impossible Triangle in IDCs: Speed, Distance, Power
Distance
High-speed transmission consumes significant power
2
Bit Error Rate (BER)¹: the core metric for IDC data communications, measuring transmission reliability.
Transmission speed ↑, distance ↑, and power consumption ↓ => BER ↑
BER
1Note: BER standard for IDC scenarios is <1e-12, representing 1 bit error per trillion bits transmitted.

## Slide 5: The Copper Speed Wall in Data Center; Breaking Through with Optical Interconnects
Chart: 
| 2020 | 2022 | 2024 | 2026
铜（Gbps/line） | 50 | 100 | 200 | 200
光模块（Gbps/line） | 50 | 100 | 200 | 400
Optical
Copper
Source: Nvidia.
1Note：InfiniBand bandwidth. NVLink transmission rate growth aligns with InfiniBand.
2Note: At 224 Gbps, copper interconnects hit a wall: unavoidable loss leads to unsustainable power and thermal costs.
​Copper (theoretical limit2):​​ 224 Gbps/line; ​
Optical (3.2T transceiver/CPO): 400 Gbps/line.
H100
A100
B100
Chart: 
| 2016 | 2017 | 2020 | 2022 | 2024
推理算力 | 19 | 130 | 620 | 4000 | 7000
训练算力 | 620 | 1987.1795 | 3477.5641
网络带宽 | 620 | 1240 | 2480
Copper => optics：224 Gbps => 400 Gbps/line
Transmission rate lags behind compute
Copper-based transmission rate: 4x in 4 years;
GPU computing power: 5.6-11x in 4 years.
Inference
11x
Training
5.6x
Bandwidth1
4x
Blackwell
7k TFLOPS
FP8
Hopper
4k TFLOPS
FP8
Ampere
620 TFLOPS
FP16
Volta
130 TFLOPS
FP16
Pascal
19 TFLOPS
FP16
1k TFLOPS
FP16
1.75k TFLOPS
FP16
800Gbps
400Gbps
200Gbps
NVLink 3.0
NVLink 5.0
NVLink 4.0
NVLink 6.0
Rubin
400G Transceiver
800G Transceiver
1.6T Transceiver
3.2T Transceiver/CPO
Gbps/line

## Slide 6
Source: Marvell, Broadcom expert call, Microsoft Research.
Inter-rack GPU interconnect: >5m;
10k-GPU clusters interconnect : km-scale.
“The practical limit for copper interconnect is 2.5m-3m, defining a cluster size ceiling of ~10,000 GPUs.”
— Broadcom expert
GPU
GPU
GPU
GPU
···
Rack & Rack
>5m
Data center interconnect
m/km-scale
Copper's effective reach at 112Gbps: ~2.5m;
Optics’ effective reach at 112Gbps : >100m.
Chart: 
| 1 | 10 | 25 | 50 | 100 | 200 | 400
Maximum Reach(m) | 25.2273 | 15.1136 | 7.1591 | 5.1136 | 3.0682 | 2 | 1
Effective Reach1(m)
2.5m
Copper
100m-2km
Optics
Copper Interconnect Reach: A Bottleneck for IDC Scaling; Optical Interconnect Breaks the Limit
1Note：the stable distance ensuring BER remains below a usable threshold.
Transmission rate
(Gbps/line)
Copper => optics： 2.5m => 100m
​​Expanding IDCs requires longer interconnects​
GPU
GPU
GPU
GPU
···
Rack & Rack
>5m

## Slide 7
Source: LightCounting
Pluggable Optics (PO): Entered Mass production in 2014; account for ~5% of HPC Capex currently. ​
Copper to pluggable：+60% power (~30W), account for 7.3% of GB200 NVL72 card power1.
​Pluggable to CPO: -60%+ module power; million-scale RMB/y saved for 10k-card cluster1.
Chart: 
 | 4 | 6.5 | 2.4
3-5
Copper
5-8
PO
2.4
CPO
60%+
-63%
“CPO primarily replaces traditional POs and does not replace copper interconnects in the short term.​​
​CPO solution reduces power consumption by 70% (33W → 9W) and lowers overall (switch) costs by 30%, offering clear competitive advantages.​​”
—Nvidia expert
Power(W/line)
Power Issues in Copper-to-Optical Transition; CPO Cuts Power Consumption Significantly
1Note：Based on the GB200 NVL72 expansion solution, totaling 9,216 B200 GPUs. The average power consumption per card in GB200 is 900W.
Power Consumption: Copper, PO, and CPO

## Slide 8: Three Consensus Optical Interconnect Solutions: PO, NPO, and CPO
Source: TSMC, Broadcom
Barriers to Adoption
Power (W) of Single 800G Port
Low
Low
High
Hight
PO (Pluggable)
22-30W
NPO (Near-Packaged)
12-18W
CPO (Co-Packaged)
5.5-9W
Short-term
Long-term
Circle size denotes the latest data rate range.​
Medium
①​ 2019: the direct path
② 2022: the gradual path
Signal loss & distortion of PCB solved
1.6T
3.2T
Switch: 102.4T
800G-1.6T/port

## Slide 9
22db
Signal loss
4db
CPO Overcomes PO’s Constrains: Signal Loss, Power Consumption, and Speed Limitations
Pluggable
CPO
Hard constraint:​​ PCB traces cause high signal loss/distortion uncorrectable under 200Gbps/line;
​Soft constraint:​​ Long-reach transmission requires power compensation (20W, 2/3 of total module power);
CPO:​​ Bypasses PCB traces, reducing loss from ​22 dB to 4 dB and cutting power by ​70%.
Source: Nvidia, Broadcom
Front view
ASIC
ASIC
Side view
PCB
Substrate
ASIC
Switch Chip
Transceiver：30W
20W (DSP) + 10W(Optical Engine)
PCB
Substrate
ASIC
Switch Chip
External Light Source
2W
Optical Engine 7W
1.6Tbps
Rate limit
12.8+Tbps
6-8cm
<1mm

## Slide 10: PO Dominates Mainstream; CPO Becomes the Focus of Tech Giants
Global giants bet on CPO：the ​most commercially viable path​ among next-gen interconnect technologies.
Key players2
CPO (Co-Packaged Optics)
Total rate
PO (Pluggable Optics)
Medium：1.6Tbps (2025)
High：6.4Tbps (2026)
Market size1
2025E
~$10bn
$10mn-scale
Source: TSMC, Insight Partners, QYResearch, Morgan Stanly Research, LightCounting
1Note：PO market size from LightCounting; CPO data from Insight Partners.
2Note：Showing only companies with the largest market share in each segment.
Domestic players dominate：Account for ​70%​​ of the top 10 global vendors.
Key players’ dynamics
CR3: 50%
100%
2024，800G shipments > 2mn units.
Q4'24: 1.6T first to certify & ship.
Q2’25: Spectrum-X CPO switch delivery.
Q2’26E: Quantum-X CPO switch delivery.
Mass commercial adoption in AIDC.
​Targeting commercialization in the 25-26 timeframe.​

## Slide 11: CPO Faces 3 Hurdles; NPO Proposed As The Bridge to CPO
Cost
NPO (Near-Packaged Optics)
Architecture
CPO (Co-Packaged Optics)
Source: Yole
ASIC Chip
Package Substrate
PCB
High-performance Substrate
ASIC Chip
OE
OE co-packaged on package substrate.
OE near-packaged on high-performance substrate.
OE
Supply Chain Maturity
Maintainability
8-10x of PO
2.5D/3D packaging brings low yield.
4-5x of PO
Based on PCB & IC packaging.
Low
Supply Chain Realignment: Deep collaboration required.​
High
Co-design & maintains the current industry structure.
Low
Full board (including ASIC) replacement.
Medium
OE and ASIC separate replacement.

## Slide 12: NPO Deployed First in IDCs; CPO As The Endgame for Aggressive Giants
Source: Broadcom, Alibaba Cloud, Guangfa Security, ServeTheHome, Yole.
400G
3.2T
PO
NPO
CPO
800G
1.6T
2021
2023
2025
2027
3.2T
6.4T
51.2T
102.4T
200G
25.6T
Future
2026
2024
2022
400G
204.8T
12.8T
409.6T
800G/1.6T
Limits of PO reached
Alibaba Cloud Data Center Deployment Roadmap
Broadcom Development Roadmap
Proposed NPO to succeed CPO 1.0
NPO advancement resumed
NPO replaced by CPO around 2028
NPO postponed

## Slide 13: IDC Interconnect by Distance: Scale-up vs. Scale-out
GPU
GPU
Copper interconnection
Optical interconnection
Optical module
Scale-out
Scale-up
Single-rack; direct & full interconnect; distance <5m;
Primarily ​copper interconnect.
Multi-node horizontal interconnect; distance >>5m;
Primarily ​optical interconnect.
NVLink
GPU
GPU
GPU
GPU
GB200 NVL72
B200 × 72 / rack
Rubin NVL288
Rubin × 288 / rack
NVLink
GPU
GPU
NVLink
Port (copper)
GPU
GPU
NVLink
GPU
GPU
NVLink
CPO Swtich
GB200 SuperPod NVL 576
GB200 NVL72 × 8
Source: Nvidia

## Slide 14: ​Overseas: CPO for Scale Out first; Domestic: CPO for Scale Up first
​CPO Initial Adoption
Overseas: Scale-out
Domestic: Scale-up
No process constraints.​​
Strong electronics
Restrictions
Industry
Advantages
14nm & chip import ban1
Strong optics
Scale Out: 2025-2026
Faster path to commercialization.
Scale Up mass production: 2027-2028
80%+
Switch/DSP chip market
Source: Changjiang Securities, Centec Communications IPO Prospectus
60%
800G optical module market
Scale Up: ~2027
Compensate for electrical weaknesses.
Amplify optical strengths

## Slide 15: Overseas: Pursue Scale-out & Scale-up Parallelly; CPO Initial Focus on Scale-out (1-2 Years)
Strategy
Scale-up roadmap
Spectrum-X
Ethernet CPO switch
Quantum-X
InfiniBand CPO switch
Scale-out roadmap
Scale-Up dominator;
Aggressively transitioning from copper to CPO.
25Q2
NVL 72 GB300
Rack-Scale Server
25.07
Rubin 288
Rack-Scale Server
26Q2
26Q2
xx
xx
Copper
CPO
Scale-Out dominator;
Betting on CPO to expand from Out to Up in 5 years.
Tomahawk 5
Ethernet CPO switch
26Q1
Full systems
Switch chips
Tomahawk 6
Ethernet CPO chip
25.06
Source: Nvidia, Broadcom.
​Scale-Out: 2025–2026​
​Scale-Up: ~2028(per Broadcom)

## Slide 16: Domestic Vendors Rely on Scale-Up to Close Performance Gap at High Power Cost
Long-cabinet CM384 requires ​6,912​ transceivers;
Scale-up consumes over 70% transceivers.
Extensive POs bring huge power consumption
Huawei CM3841 vs. NVIDIA GB200 NVL72
Source: Nvidia, Huawei, SemiAnalysis;
1Note：CM384 = CloudMatrix 384 (384x Ascend 910C NPUs), to benchmark against the GB200 NVL72;
2Note: Transceiver power consumption is based on 10W (400G PO); Ascend 910C single-card power ≈800W.​
Rack×16 > 2.5m
Chart: 
 | 2500
 | 780
Single-Card BF16 Compute Performance (TFLOPS)​
-69%
Chart: 
 | 180
 | 300
Overall Compute Performance (TFLOPS)​
+67%
Chart: 
 | 1536 | 5376
Scale-out
Scale-up
CM384 Transceiver Quantity
Per card: ≈1/3 of NVIDIA B200;
Full cluster: ≈1.7x of NVIDIA B200.
GB200 NVL72
Huawei CM384
Chart: 
 | 1.86 | 1.63 | 1 | 0.81 | 0.81
 | 0.23 | 0.63 | 0.19
CM384
Transceiver contribution
Single-card contribution
Remaining gap
GB200 NVL72
-56%
W/TFLOPS
CM384 consumes +200% power per TFLOP than NVL72, transceivers represent 20% of this gap2.

## Slide 17
① Potential Ports: GPUs/ASICs + switches using 800G/1.6T/3.2T transceivers. 2030E shipments: ​100mn.
② Penetration Rate: Supported by new HPC cluster construction. 2030E penetration: 40%.
Source: Morgan Stanley Research, LightCounting, SemiAnalysis, Broadcom expert.
CPO: A Multi-Billion Dollar Market Paved by Data Rate Scaling
Base case
CAGR 172%, 2030E Revenue: ~$9.3bn;
NVIDIA Rubin + Broadcom TH7 lead high-end pluggable module replacement; penetration ~40%.
Bull case
CAGR 210%, 2030E Revenue: ~$27bn;
CPO becomes mainstream in 800G/1.6T nodes; penetration >60%, extends to 400G.
Bear case
CAGR 107%, 2030E Revenue: ~$1B;
Piloted only in ultra-high-end AI clusters; penetration ≤15%.
CPO Scale
=
Potential Ports
×
Penetration Rate
×
Unit Price
①
②
New IDCs prefer CPO to avoid future replacement costs
Amazon, Meta, Google, x.AI require optical interconnects for 10k-clusters
“35% of Meta’s HPC cluster interconnects have applied CPO.”
— Broadcom expert

## Slide 18: CPO Key Modules: Silicon Photonics Chip, Electrical IC, Switch ASIC, and Integration & Delivery
External Light
Routing + Conversion (Optical ↔ Electrical)
Amplification + Optimization
Laser
② Electrical Signal Hub
③ Switch Chip
Input/Output
① Optical Signal Hub
Control + Signal Processing
Fiber
Silicon Photonics Chip
(SiPh)
​Electrical IC
(EIC)​
Interposer
ASIC
④ Integration¹: Advanced Packaging + System Integration
1Note: Foundry not included.

## Slide 19: Supply Chain: EICs & Switch Chips - Large Scale, High Margin, Long R&D
① Optical Signal Hub
② Electrical Signal Hub
③ Switch Chip
Market Size1（2028E）
R&D Cycle
Source: Yole, TechNavio, Huaxin Securities, Broadcom, TSMC, Inphi, ASE, Innolight.
1Note: Scope limited in data-com market.
10-20%
$bn
CAGR: 40+%
20-30%
CAGR: 20+%
Gross
Margin
40%
50-70%
5y
4y
DSP 3y/gen
2015-2025
40-70%
2020-2025
2017-2024
④ Integration
CAGR: 15+%
10-50%
5y
3y
20-30%
CAGR: 10+%
2015-2024
2020-2025
2-3y/gen
2005-2012
Over-
seas
China
7y
10y
7y
9y
10-20%
$bn
$bn
$bn
BOM

## Slide 20: ​Supply Chain Focus: Broadcom-Led Integrated Giants and Strategic Domestic Startups like FiconTEC
Global Leading Players
Global Key Startups
Source: Yole
Domestic Key Startups
Prototype Phase
① Optical Signal Hub
② Electrical Signal Hub
③ Switch Chip
④ Integration
Tencent JDM
Delivery Phase
Switch
Assembly and Test
光模块
SiPh
Laser

## Slide 21: Broadcom: First to Commercialize CPO with a Sustained Lead
Source: Broadcom, Nvidia, Intel, Cisco, Marvell;
1Note: CPO switch chips prioritized in timeline.
Competitive Positioning: ≈1-year lead over ​NVIDIA;
The only vendor with publicly confirmed mass production of CPO switches/chips;​
  TH4 & TH5: Industry’s first CPO switch chips to enter volume production.
12.8
25.6
51.2
102.4
ASIC
Capacity（Tbps）
2021
Announced
TH4
2023
Demo
TH5
2020
Demo
WEDGE
Broadcom edge
~1 year
2022
Joint Deployment
TH4
Announced
TH5
Teralynx
Demo
2024
Mass production
TH5
Teralynx10
Mass production (not CPO)
2025
25.06
Mass production
TH6
26
Mass production
Spectrum 6
Announced
Mass production
Spectrum 5
Timeline of CPO Switch Chip Milestones1 (2020–2025)​

## Slide 22: Broadcom: The Most Comprehensive CPO Capability Profile
Broadcom | Nvidia | Intel | Cisco | Marvell
高 | 高 | 高 | 中 | 中
高 | 高 | ​高 | 中 | 中
高 | 高 | 高 | ​中 | 低​
​高​ | 中 | 低 | 低 | 低
Capability Profile of Integrated Giants Across the CPO Value Chain1
Medium
High
Design
Assembly & Test
Low
Broadcom leads the CPO ecosystem with strongest capabilities.
Final
Packaging
Foundry
Source: Broadcom, Nvidia, Intel, Cisco, Marvell;
1Note: Not an exhaustive list; focusing on key partners.​

## Slide 23: Why Broadcom Bets on CPO: Aligning with HPC's In-House ASIC Trend + Network Support for Ecosystem Positioning
Amazon
MSFT
Intel
Source: Nomura Securities, J.P.Morgan, Fubon Research, BNP
Chart: 
| 2024 | 2025 | 2026
 | 20 | 33 | 50
 | 80 | 67 | 50
 | 11 | 18.15 | 27.5
>33
Shipment Portion（%）
26E, ASIC surpass GPU
Google
Meta
ByteDance
Google
Meta
ByteDance
OpenAI
xAI
ASIC
GPU
Broadcom ASIC
2025E Main ASIC Vendors’s Shipment
Amazon
MSFT
Intel
① ASIC: The inevitable trend. Broadcom plays a central role.
HPCs seek computing autonomy & cost control​ → More players partner with Broadcom;
​​OpenAI, xAI: New volume production orders in 2026 will ​bring forward the “ASIC > GPU” inflection point from 2027–28 to 2026.
Chart: 
 | 39.4737 | 52.6316 | 7.8947
Amazon
Google
Meta
100-300k units
1400-1500k units
1500-2000 units

## Slide 24: Why Broadcom Bets on CPO: Aligning with HPC's In-House ASIC Trend + Network Support for Ecosystem Positioning
Source: Fubon Research, Semiconductor Research, LightCounting
Chart: 
| 20089 | 19723 | 19358 | 18993 | 18993
 | 5000 | 2200 | 1979 | 1979 | 312
 | 2307 | 918 | 196.5 | 1310 | 667 | 177 | 51.2
 | 2615 | 5000 | 4600 | 1835 | 432
 | 800 | 320
23
24
25
26
22
Year of Mass Production
BF16/FP16 (TFLOPS)
GB200
B200
H200-SXM
H100-SXM1
A800-SXM
Google-TPU v6e
Google-TPU v5p
AWS-Trainum3
AWS-Tranium2
Meta-MTIA V2
Meta-MTIA V1
AMD-MI325x
AMD-MI355X
AMD-MI350X
Intel-Gaudi3
Intel-Gaudi2
Ascend 910C
Ascend 910B
Google-​TPU v7p​
GPU
ASIC/xPU
General-Purpose Compute Card
Huawei
42%
46%
34%
② ASIC: Weaker per-card performance, requiring optical interconnect & CPO when scaling.
Top ASIC per-card performance ≈ ​40% of same-gen GPU​ (similar to domestic Scale-up logic);
Cloud ASICs expected to drive ​~80% of transceiver market growth; leaders like ​Google, Amazon​ now evolving toward ​CPO.
Reserving CPO interfaces

## Slide 25: FiconTEC: Key Player for Domestic Substitution in CPO
Source: Robo-Technik
Market Position: One of the very few global supplier for automated SiPh/CPO module assembly & test;
​Prospects: Unmatched high-precision packaging capability, crucial for CPO era.
Acquired 100% by Chinese listed company Robotechnik for RMB 1.01bn.
Seed-round investment.
Founded in Germany.
2001
2002
2025
Chart: 
| 微组装 | 自动化测试
 | 0.7829 | 0.2171
Micro-assembly
Revenue Breakdown (2023A)
Test Equipment, etc.
Test, clean, and repair all-in-one
ASSEMBLYLINE Series
World-leading accuracy
2025.06
2021
Business: Dominator of micro-assembly & automated testing
Roadmap: Filling a key domestic technology gap
2023
Robotechnik announced a plan to acquire 100% of ficonTEC.

## Slide 26: FiconTEC: Key Player for Domestic Substitution in CPO
Capacity 94 units
Output 80 units
Sales 96 units
Source: Robo-Technik
Global Delivery
700+ units
ASP
RMB
2.35mn
Tech Group AS
Standard- hardware
Delivery：Low-volume, high-price, heavy on delivery.
Chart: 
| 2021 | 2022 | 2023
Revenue (left) | 2.79 | 2.87 | 2.57
Net Profit Margin (left) | -0.58 | -0.22 | -0.14
Gross Margin (right) | 0.344 | 0.416 | 0.402
Gross margin: ~40%, exceeds the industry average for assembly and test (approx. -30%);
Losses: continue to narrow.
Capacity Utilization Rate
85%
Customers & Suppliers: Concentrated.
$0.1bn
Chart: 
| 前五大客户 | 其他
 | 0.42 | 0.58
CR5
Customer Proportion
Chart: 
| Tech Group AS | 其他
 | 0.38 | 0.62
Supplier Proportion
Upstream & Downstream
Profitability

## Slide 27
Business
&
Products
Advantages
Progress
2024.10：Shipped 15k chiplets in the past 18 months;
26E：First high-volume customers.
OIO Chiplet
Technology integrated into PCIe 6.0 standard;
Ecosystem barrier.
2015US
2020US
2017US
Funding
512Gbps OIO bandwidth
Ultra-low power: 4.9pJ/bit
1B
2024.12 Series D: $155mn
POC => Mass Production
25H2: Sampling starts,
2027: mass production.
Systematic OIO with long R&D cycle;
Cross-layer solution.
2025.02 Series C1: $250mn
Certify => Design-in / Early Proto
2025 Summer: interposer shipment;
2026: L200 CPO chiplet shipment.
Compatible with Broadcom;
Abstracts packaging layer into hardware (controllable delivery).
2024.10 Series D: $400mn
Certify => Design-in
TeraPHY
​Optical Full-Stack Solutions
Card：PFLink，14.4 Tbps/die
Switch：PFSwitch
Photonic Fabric
CPO/OIO Passage Interposer
Passage Series
2.5B
4.4B
Proprietary silicon photonics chip
Package-level solution
CPO Startups Comparison: Ayar Labs, Lightmatter, Celestial AI
Strategic Investor

## Slide 28: Summary

## Slide 29: DeepSeek: Domestic LLM Restricted by GPU Interconnection Bandwidth, CPO as Priority Exploration Direction
Source: Deepseek
CPO: A Crucial Solution
H800 Bandwidth Restricts Training and Inference
H800 Bandwidth Halved Compared to H100
① Network architecture: Forced to use scale-out to compensate for scale-up limitations;
② Training strategy: Tensor parallelism abandoned due to bandwidth constraints;
③ Inference speed: MoE inference rate is 1/20th of H100.
①
②
③
Notes: 1. DS

## Slide 30: DeepSeek: H800 Bandwidth and Inference Rate
Chart: 
 | 1800 | 900 | 400 | 200
B200
H100
H800
H20
-56%
Inter-card Bandwidth（GB/s）
Source: Deepseek, Nvidia, Huawei
Chart: 
 | 400 | 900
 | 67 | 1200

H800 (DeepSeek)
GB200 NVL72
~18x
Inter-card Bandwidth (GB/s)
Inference Rate (token/s)
① H800 bandwidth halved compared to H100 ;
② If bandwidth returns to the level of B200, the inference rate will increase to ~18 times the original.
Notes: 1. DS

## Slide 31: Overseas Strong in Electricity, Weak in Optics; Domestic Vise Versa - Industry Evidence
DSP1
7nm-3nm
800G Transceiver1
Packaging/>100nm SiPh
Process Ban
High
Global Market Share
Low
High
Source: Changjiang Securities, Centec Communications IPO Prospectus;
1Data Sources:​​ 800G Transceivers (2025E) | OSAT (2024A) | Switch Chips (2020A) | Electrical DSP Chips (Aug-2023, 50G/100G).
Switch Chip1
16nm-5nm
OSAT1
Limited process ban
Innolight
36%
Eoptolink
23%
Coherent
21%
Mellanox
4%
Accelink&HG
4%
ASE
45%
Amkor
16%
JCET
11%
TFME
8%
Marvell
20%
5nm
Broadcom
62%
5nm
Realtek
16%
Centec
1.6%
16nm
Marvell
65%
3nm
Broadcom
20%
3nm
Credo
<5%
3nm
Domestic
Overseas
Optics
Electronics

## Slide 32: Broadcom CPO Industry Chain
Source: Broadcom.
Customers
Switch Chip Wafer
EIC Wafer
SiPh Wafer
Switch Chip + CPO
Switch Chip + CPO + Lens
CPO Switch
Laser Chip
ELS Laser Module
Fiber
Design
Foundry
Packaging
Optoelectronic Integration
Final Assembly

## Slide 33: CPO Map
Design House
Foundry
OSAT
Transceiver
Equipment
Operator
eIC
Switch
ASIC
SiPho
Laser