## Slide 1
Source: LightCounting, Nvidia, Broadcom.
Pluggable Optics (PO): Entered mass production in 2014. ​
Copper to pluggable: 50% power consumption increase, accounting for 7.4% of GB200 NVL72 card power2.
​Pluggable to CPO: ~40% system-level power cut3; 5- mn RMB/y saved for 10k-card cluster2.
Chart: 
 | 1 | 10 | 15 | 5.5
PO
CPO
< 0.1
Power (W per 800G port)
Note 1: The transmission reach of DAC is less than 2 meters. AEC integrates signal enhancement chips (re-timer) to extend the reach (5 meters) using more power.
Note 2: Consider GB200 NVL72 cluster with 9,216 B200 GPUs with 2-layer interconnect.
Note 3: At the 2025 Optica Executive Forum held in March, Broadcom demonstrated power savings of CPO in full 64-port system tests.
Power consumption: Copper, Pluggable, and CPO
Long reach
(> 5 m)
Short reach
(≤ 5 m)
Copper
Optical
Direct Attach Copper Cable (DAC1)
Active Electrical Cable
(AEC1)
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
The power issue in the copper-to-optical migration is cut significantly by CPO
Notes: 现有功耗数据是单模，单模是趋势
800G AEC 10W（5m），5W有可能是half架构
单模是未来趋势，多模速率难提升（224G）
功耗测算逻辑：
9216 GPU -> 9216 800G光模块 + 14400 1.6T光模块
光模块->CPO的系统级功耗节约（考虑交换机）：800G 22W，1.6T 48W （）
总功耗节约：900 kW
年电费节约：5.5 mn RMB