## Slide 1: From pluggable to co-packaged optics: an intro to IDC interconnect
Oct 2025

## Slide 2: Table of contents
Lorem ipsum dolor
01. Background: why CPO?
02. Why the transition from copper to optical, and from pluggable to CPO?
03. Where CPO fits first: scale-up or scale-out?
04. How big is the CPO market?
05. How does the CPO value chain look?
Lorem ipsum
Lorem ipsum
06. Key players to watch: Broadcom, and emerging players
Tech
Markets

## Slide 3: Why the focus on CPO?
IMAGE
Pivot from copper to optics
Launch 2 CPO switches in Mar 25
Premiere advanced CPO switches
GTC 2025
IMAGE
Bandwidth limitations restrict training, inference, and network scalability
CPO could deliver higher bandwidth and enhance energy efficiency (published in May 25)
《Insights into DS-V3》
Highlight CPO’s importance under limited bandwidth
Tomahawk Switches
IMAGE
Tomahawk 4: 1st CPO switch chip announced in 2021
Tomahawk 6: fastest CPO switch chip, announced in Apr 25
Accelerate CPO ecosystem adoption

## Slide 4
Distance
Long-reach transmission demands high power; low power limits reach.
1
3
Power
Long-distance suffers signal attenuation, requiring power compensation.
2
BER
Note 1: BER standard for IDC scenarios is <1e-12, representing 1 bit error per trillion bits transmitted.
System goal: Given a Bit Error Rate1 (BER, the core transmission reliability metric in IDC data communications) target, optimize the tradeoff among speed, distance and power
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Communication trade-off triangle in IDCs: speed, distance, and power
Speed
Low power + extended distance requires reduced data rates or bandwidth.
Domestic market prioritize speed over power (not a constraint).
WIP

## Slide 5
Source: Marvell, Broadcom expert call, Microsoft Research.
···
Data center interconnect
m/km-scale
Chart: 
| 1 | 10 | 25 | 50 | 100 | 200 | 400
Maximum Reach(m) | 25.2273 | 15.1136 | 7.1591 | 5.1136 | 3.0682 | 2 | 1
Effective reach1(m)
~2.5 m at 112 Gbps
Copper
> 100 m
Optics
Note 1: 112 Gbps is the current mainstream rate, while 224 Gbps is now emerging.​
Note 2: The stable distance ensuring BER remains below a usable threshold.
Transmission rate
(Gbps/line)
Optics significantly increases effective reach
​​Expanding IDCs relies on optical interconnect​
GPU
GPU
GPU
GPU
···
Inter-rack
> 5 m
Intra-rack
< 5 m
GPU
GPU
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Optical interconnect overcomes the bottleneck of copper reach in IDC scaling
Copper dominates
Optics dominate
Optics dominate
at 112 Gbps
Notes: 右边的铜为无源铜缆（安费诺、立讯）
Scale up上限目前看为nvl72，顶多一百多
Meta dsf 全部用光

## Slide 6
Source: LightCounting, Nvidia, Broadcom.
Pluggable Optics (PO): Entered mass production in 2014, accounting for ~5% of HPC capex currently. ​
Copper to pluggable: 50% power consumption increase, accounting for 7.4% of GB200 NVL72 card power2.
​Pluggable to CPO: ~40% system-level power cut; 5- mn RMB/y saved for 10k-card cluster2.
Chart: 
 | 1 | 10 | 15 | 5.5
PO
CPO
< 0.1
Power (W per 800G port)
Note 1: The transmission reach of DAC is less than 2 meters. AEC integrates signal enhancement chips (re-timer) to extend the reach (5 meters) using more power.
Note 2: Consider GB200 NVL72 cluster with 9,216 B200 GPUs with 2-layer interconnect.
Power consumption: Copper, Pluggable, and CPO
Long reach
(> 5 m)
Short reach
(≤ 5 m)
Copper
Optical
Direct Attach Copper Cable (DAC1)
Active Electrical Cable
(AEC1)
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
The power issue in the copper-to-optical migration is cut significantly by CPO
Notes: 现有功耗数据是单模，单模是趋势
800G AEC 10W（5m），5W有可能是half架构
单模是未来趋势，多模速率难提升（224G）
功耗测算逻辑：
9216 GPU -> 9216 800G光模块 + 14400 1.6T光模块
光模块->CPO的系统级功耗节约（考虑交换机）：800G 22W，1.6T 48W 总功耗节约：900 kW
年电费节约：5.5 mn RMB

## Slide 7
Chart: 
| 2016 | 2017 | 2020 | 2022 | 2024
推理算力 | 19 | 130 | 620 | 4000 | 7000
训练算力 | 620 | 1987.1795 | 3477.5641
网络带宽 | 620 | 930 | 1860
Copper interconnect transmission rate eclipsed by optical interconnect
Chart: 
| 2020 | 2022 | 2024 | 2026
铜（Gbps/line） | 50 | 100 | 200 | 200
光模块（Gbps/line） | 50 | 100 | 200 | 400
Optical
Copper
Source: Nvidia.
Note 1: NVLink bandwidth per card.
Note 2: At 224 Gbps, copper interconnects hit a wall, and unavoidable loss leads to unsustainable power and thermal costs.
H100 (NVLink 4.0)
A100 (NVLink 3.0)
B100 (NVLink 5.0)
​Optical hits 448Gbps, leaving NVLink at 224Gbps
Transmission rate growth lags behind compute
Inference
11x
Training
5.6x
Bandwidth1
3x
Blackwell
7k TFLOPS
FP8
Hopper
4k TFLOPS
FP8
Ampere
620 TFLOPS
FP16
Volta
130 TFLOPS
FP16
Pascal
19 TFLOPS
FP16
1k TFLOPS
FP16
1.75k TFLOPS
FP16
1800GB/s
900GB/s
600GB/s
Rubin (NVLink 6.0)
400G Transceiver
800G Transceiver
1.6T Transceiver
3.2T Transceiver/CPO
Gbps/line
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
300GB/s

## Slide 8
Copper-to-optical migration: players adopt different roadmaps within optical interconnect
CPC + LPO
Co-Packaged Copper
Linear-drive Pluggable
~10W
Source: TSMC, Broadcom, Meta, Huawei
Time
Power (W) per 800G port
Low
High
PO (Pluggable)
~15W
NPO (Near-Packaged)
~9W
CPO (Co-Packaged)
~5.5W
Short-term: non-consensus
Long-term
Circle size denotes the latest data rate range.​
I. 2019: the direct path
II. 2022-2025: the gradual path
1.6T
3.2T
Switch: 102.4T
800G-1.6T/port
1.6T
Today
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
WIP
Notes: LPO 隐性成本高，稳定性并不理想；线性架构导致性能（连通性）没有那么高
NPO 压接，非毁坏
OCS很难用，需要对模型流量和卡非常了解，技术难点太高。单层级非常大的组网规模可用（可以看一下量）
Scale up以后从铜转光的重要原因：
面板上无法容纳光模块过多数量
GPU功耗很高，无法容纳高能耗的互联
时延

## Slide 9
22dB
Signal loss
4dB
Pluggable
CPO
CPO:​​ By bypassing PCB traces, it reduces loss from ​22 dB to 4 dB and cuts power by ​70%
Hard constraint:​​ PCB-induced loss/distortion becomes uncorrectable beyond 200 Gbps/line
​Soft constraint:​​ Long-reach transmission requires power compensation
Source: Nvidia, Broadcom.
Note 1: Power consumption in 1.6T port (from Nvidia).
Front view
ASIC
ASIC
Side view
PCB
Substrate
ASIC/GPU
Transceiver: 30W1
20W (DSP) + 10W(Optical engine)
PCB
Substrate
ASIC/GPU
External light source
2W
Optical engine1 7W
1.6-3.2Tbps
Total rate limit
> 102.4Tbps
(16 × 6.4T)
6-8cm
<1mm
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
CPO overcomes PO’s constraints: signal loss, power consumption, and speed limitations
Co-packaging adds expense and maintenance challenges
WIP

## Slide 10
Global giants bet on CPO: viewed as the ​most commercially viable path​ for next-gen interconnect technologies.
Key players2
CPO (Co-Packaged Optics)
Total rate
PO (Pluggable Optics)
1.6Tbps
6.4Tbps
Market size1
2025E
~$10bn
mn-scale
Source: TSMC, Insight Partners, QYResearch, Morgan Stanley Research, LightCounting.
Note 1: PO market size from LightCounting; CPO data from Insight Partners.
Note 2: Showing only companies with the largest market share in each segment.
Domestic players dominate: account for ​70%​​ of the top 10 global vendors.
Dynamics
800G CR3: 80%
2024: 800G shipments > 2mn units
Q4 25: 1.6T first to certify & ship
Q4 25: Quantum-X CPO switch volume production
H1 26: Spectrum-X CPO switch volume production
Mass commercial adoption in AIDC.
​Targeting commercialization in the 25-26 timeframe.​
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
If CPO adopts in the long run, global giants may gain supply chain leverage

## Slide 11
GPU
GPU
Copper interconnect
Optical interconnect
Optical module
Scale-out
Scale-up
Single-node direct & full interconnect (≤ 5 m);
Bandwidth: TB/s; Latency: sub-μs;
Primarily ​copper interconnect.
Multi-node horizontal interconnect (≫ 5 m);
Bandwidth: GB/s; Latency: ms;
Primarily ​optical interconnect.
NVLink
GPU
GPU
GPU
GPU
GB200 NVL72
B200 × 72 / rack
Rubin NVL288
Rubin × 288 / rack
NVLink
GPU
GPU
NVLink
Port (copper)
GPU
GPU
NVLink
GPU
GPU
NVLink
Switch
GB200 SuperPod NVL 576
GB200 NVL72 × 8
Source: Nvidia
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
IDC interconnect by distance: scale-up vs scale-out
WIP
Notes: Rubin Ultra NVL576: 144x GPUs with 576 dies;
GB200 NVL72: 72 GPUs.

## Slide 12
Overseas
Domestic
No process constraints.​​
Strong in electronics
14nm & chip import ban
Weak in electronics
Transmission reach matters
Easier to commercialize
> 80%
Switch/ DSP chips
Source: Changjiang Securities, Centec Communications IPO Prospectus, Sitrus Official Web Site.
Note 1: Sitrus and Centec are two leading Chinese companies specializing in high-speed DSP chips and switch chips, respectively.
< 5%
Switch/ DSP chips1
Chip limitations drive longer-reach scale-up solutions
Weak in electronics, making optical essential for scale-up
Starting testing of optical in IDCs
Copper still dominates in the short-term
Scale-out
Initial adoption
Acceleration
Scale-up
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
​Optical interconnect adoption prioritized in scale-out and accelerated in scale-up
Aggressive push
Notes: Sitrus、盛科备注
CPO线性对serdes要求更高
Scale up的光可能更快发生：OCP

## Slide 13
Scale-up
Spectrum-X
Ethernet CPO switch
Quantum-X
InfiniBand CPO switch
Scale-out
H1 26: Volume production
NVL 72 GB300
Rack-scale server
Q3 25: Volume production
NVL 576 Rubin
Rack-scale server
H1 26: Volume production
Q4 25: Volume production
xx
xx
Copper
CPO
Tomahawk 5
Ethernet CPO switch
H2 24: Sampling and Testing
Full systems
Switch chips
Tomahawk 6
Ethernet CPO chip
Oct 25: Sampling and Testing
Source: Nvidia, Broadcom, Nomura research, BNP.
Note 1: Volume production date.
Volume production timeline: ​Scale-out in 2026​; Scale-up in 2028 (per Broadcom)
CPO adoption may delay due to gaps in supply chain maturity and maintainability compared to PO
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Overseas pursue scale-out and scale-up in parallel, with CPO initially focused on scale-out for 1-2 years
Notes: Broadcom TH 5 CPO switch’s first customers: Meta, Tencent, Bytedance. Meta正在小规模试验点，稳定性有待商榷（BER相比PO低两到三个数量级，但比TH 4高 2-3个数量级）

## Slide 14
Potential ports2
Penetration rate5
Unit Price6
CPO scale1
: ~$6 bn in 2028
800G+ transceiver shipments
GPU shipments2
ASIC shipment4
Transceiver attach ratio3
Transceiver attach ratio3
GPU ports
ASIC ports
Chart: 
 | 1 | 5 | 1
 | 2 | 4 | 8
 | 0 | 3 | 15
0
10
20%
26E
27E
1%
8%
15%
28E
800G
1.6T
3.2T
800G+ transceivers => CPO
Per-port CPO value
Nvidia Quantum CPO switch: $120-130k with 144 800G ports -> ~$700 / port in 2025;
Price descending accelerates in 2027 as CPO starts penetration.
Source: HSBC2, Goldman Sachs3, 4, 6, Citi5.
Note 1: The model focuses primarily on the calculation logic, given that GPU/ASIC shipments and transceiver attach ratios are highly scenario-dependent.
CPO starts penetration in late 2027: 1 year for mass production & half year for HPC adoption
Rubin (1.8 mn) and Rubin Ultra (3 mn) replace Hopper and Blackwell.
~ 57mn
~10%
~$1000
~5 mn
~ 5 : 1
~6.3 mn
~ 5 : 1
3 : 1 -> 5 : 1. Rubin requires twice the number of transceivers compared to GB300 (~3x 1.6T transceivers / card).
3 : 1 -> 5 : 1, driven by lower performance per card and increased cluster networking complexity.
~55% of total datacenter AI chip volumes (Google TPU: > 4mn in 2028 with a shipment share of ~70%);
~26 mn
~31 mn
Key assumptions
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Estimating the CPO market: driven by port growth and data rate scaling
WIP
Notes: 光模块配比：线性+阶跃
1层：几百到几千，1:3
2层：万卡，1:5
3层：大几万卡
谷歌TPU出货量：2025, 2-2.5mn，占75%（份额预计长期保持）
博通TH6 CPO芯片报价：可能为$20k，BOM占比20-30%，整机价格$60-100k

## Slide 15
Global leading players
Global key startups
Source: Yole
Domestic key players
① Optical signal Hub
② Electrical signal Hub
③ Switch chip
④ Integration
Tencent JDM on POs
Switch
Assembly and test
SiPh
Laser
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
The supply chain is early-stage, with most players in initial strategic layout

## Slide 16
64% of ASIC shipment
Source: Nomura Securities, J.P.Morgan, Fubon Research, BNP.
Chart: 
| 2024 | 2025 | 2026
 | 38 | 41
2024
2025
2026E
Accelerator chips shipment unit share (%)
ASIC
​ASIC: High costs, limited TSMC supply;
​Nvidia continues to dominate AI cloud compute.​
Pessimistic scenario
Optimistic scenario
New orders from OpenAI & xAI;
Bring forward the “ASIC > GPU” inflection point from 2027–28 to 2026.
40
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Broadcom’s CPO bet: ASIC becomes the long-term trend, and Broadcom plays a central role
62% of ASIC shipment
60
WIP
Notes: 第一代样机TH4已在机房跑测试
TH5正在测试，还没测完，Meta的数据来看还需要打磨稳定性（误码率1e-9、误码分布是否在纠错码的纠错范围内+Buff
er）
ASIC 43%的share在26年比较fair
计算卡出货量（mn）2024 2025E
GPU 450 550
ASIC 280 390
Amazon 80 120
Google 180 220
Meta 0 20
Others 20 30

## Slide 17
Source: Fubon Research, Semiconductor Research, LightCounting.
Chart: 
| 20089 | 19723 | 19358 | 18993 | 18993
 | 5000 | 2200 | 1979 | 1979 | 312
 | 2307 | 918 | 196.5 | 1310 | 667
 | 2615 | 5000 | 4600 | 1835 | 432
 | 800 | 320
23
24
25
26
22
Year of mass production
BF16/FP16 (TFLOPS)
GB200
B200
H200-SXM
H100-SXM1
Google-​TPU v7p​
Google-TPU v6e
Google-TPU v5p
AWS-Trainum3
AWS-Tranium2
AMD-MI325x
AMD-MI355X
AMD-MI350X
Intel-Gaudi3
Intel-Gaudi2
Ascend 910C
Ascend 910B
A800-SXM
GPU
ASIC/xPU
General-purpose compute Card
Huawei
42%
46%
34%
ASIC: Weaker per-card performance, requiring optical interconnect (CPO) when scaling.
Top‑end ASICs deliver ~40% of same‑gen GPU throughput​; Cloud ASICs could drive ​~80% of transceiver market growth;
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Broadcom’s CPO bet: ASIC relies more on optical interconnect, and Broadcom attempts to lock in the data center ecosystem
WIP
Notes: 博通：通过CPO绑定光、电芯片，产业链绑定

## Slide 18
Business
&
products
Advantages
Progress
Dec 24: Shipped 15k chiplets in the past 18 months;
26E: First high-volume customers.
Optical I/O (OIO) chiplets.
Technology integrated into PCIe 6.0 standard;
Ecosystem barrier.
2015US
2020US
2017US
Funding
512 Gbps OIO bandwidth
Ultra-low power: 4.9pJ/bit
1B
Series D (Dec 24): $155mn
POC -> Mass production
H2 25: Sampling starts;
27E: Mass production.
Systematic OIO with long R&D cycle;
Cross-layer solution.
Series C1(Feb 25): $250mn
Certify -> Design-in / Early proto
25 Summer: Interposer shipment;
26E: L200 CPO chiplets shipment.
Compatible with Broadcom;
Abstracts packaging layer into hardware (controllable delivery).
Series D (Oct 24): $400mn
Certify -> Design-in
TeraPHY
​Optical full-stack solutions.
Card: PFLink，14.4 Tbps/die
Switch: PFSwitch
Photonic Fabric
CPO/OIO passage interposer.
Passage Series
2.5B
4.4B
Proprietary silicon photonics chip
Package-level solution
Strategic investor
1
Note 1: Lightmatter (CEO: Nicholas Harris) and SuiJi Technology (a Chinese optical compute company invested by Tencent. CEO: Yichen Shen), spin-off from the same MIT team.
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Startups with a long-term vision in optical: Ayar Labs, Celestial AI, and Lightmatter
WIP

## Slide 19
Source: Robotechnik.
Supply chain position: One of the very few global suppliers for automated SiPh/CPO assembly & test;
​Domestic substitution: Fully acquired by Chinese companies Robotechnik in 2025
Chart: 
| 微组装 | 自动化测试
 | 0.7829 | 0.2171
Micro-assembly
Revenue breakdown
(23A)
Test equipment, etc.
Test-to-repair
All-in-one
AL-Series
Business
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
FiconTEC: Key player for domestic substitution in CPO
~40% gross margin, exceeds the industry average for assembly and test (~30%)
10k RMB
Profitability
Vied for by Nvidia and TSMC
FiconTEC is the key supplier of Nvidia, TSMC, and Broadcom in SiPh/CPO
Sole supplier of Broadcom’s CPO optical coupling equipment
Chart: 
| 2022 | 2023 | Jan 2024 - Jul 2024
Revenue (left) | 28668.07 | 38244 | 12807.96
Net profit (left) | -62.61 | 2900.4 | -2481.16
Gross margin (right) | 0.4163 | 0.4162 | 0.4064
WIP

## Slide 20: Summary
Trend: "Optics-in, Copper-out" is the established path for high-speed data center interconnects
Scenario: Optical interconnect get adopted first in scale-out, with accelerated penetration in scale-up
Roadmap: CPO is the long-term bet, while near-term solution is not determined.​
Notes: 光进铜退
场景：光会先在scale out
路径：长期CPO短期不明朗

## Slide 22
Domestic vendors rely on scale-up to close performance gap at high power cost
Long-cabinet CM384 requires ​6,912​ transceivers;
Scale-up consumes over 70% transceivers.
Extensive POs bring huge power consumption
Huawei CM3841 vs. NVIDIA GB200 NVL72
Source: Nvidia, Huawei, SemiAnalysis.
Note 1: CM384 = CloudMatrix 384 (384x Ascend 910C NPUs), to benchmark against the GB200 NVL72.
Note 2: Transceiver power consumption is based on 400G POs; Ascend 910C single-card power ≈ 800W.​
Rack×16 > 2.5 m
Chart: 
 | 2500
 | 780
Single-Card BF16 Compute Performance (TFLOPS)​
-69%
Chart: 
 | 180
 | 300
Overall Compute Performance (TFLOPS)​
+67%
Chart: 
 | 1536 | 5376
Scale-out
Scale-up
CM384 Transceiver Quantity
Per card: ~⅓ of NVIDIA B200;
Full cluster: ~1.7 x of NVIDIA B200.
GB200 NVL72
Huawei CM384
Chart: 
 | 1.86 | 1.63 | 1 | 0.81 | 0.81
 | 0.23 | 0.63 | 0.19
CM384
Transceiver contribution
Single-card contribution
Remaining gap
GB200 NVL72
-56%
W per TFLOPS
CM384 consumes +200% power per TFLOP than NVL72, transceivers represent 20% of this gap2.
Why
Tech
What
Market
Where
Sizing
Value Chain
Players

## Slide 23
External light
Routing + conversion (optical ↔ electrical)
Amplification + optimization
Laser
② Electrical signal hub
③ Switch chip
Input/Output
① Optical signal hub
Control + signal processing
Fiber
Silicon Photonics Chip
(SiPh)
​Electrical IC
(EIC)​
Interposer
ASIC
④ Integration: advanced packaging + system integration
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
CPO key modules: Silicon photonics (SiPh), electrical IC (EIC), switch ASIC, and integration & delivery

## Slide 24
① Optical signal hub
② Electrical signal hub
③ Switch chip
Market size1（2028E）
R&D cycle
Source: Yole, TechNavio, Huaxin Securities, Broadcom, TSMC, Inphi, ASE, Innolight.
1Note: Scope limited in data-com market.
10-20%
$bn
CAGR: 40+%
20-30%
CAGR: 20+%
Gross
margin
40%
50-70%
DSP 3y/gen
2015-2025
40-70%
SiPh: 5y/gen
2017-2024
④ Integration
CAGR: 15+%
10-50%
20-30%
CAGR: 10+%
2015-2024
2.5/3D: 5y
2-3y/gen
2005-2012
Over-
seas
Dom-estic
10-20%
$bn
$bn
$bn
BOM
(Acquired by Marvell）
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Supply chain: EICs & switch chips - large scale, high margin, long R&D
Notes: 删y

## Slide 25
Broadcom | Nvidia | Intel | Cisco | Marvell
高 | 高 | 高 | 中 | 中
高 | 高 | ​高 | 中 | 中
高 | 高 | 高 | ​中 | 低​
​高​ | 中 | 低 | 低 | 低
Capability profile of integrated giants across the CPO value Chain1
Medium
High
Design
Assembly & test
Low
Broadcom leads the CPO ecosystem with strong capabilities.
Final
packaging
Foundry
Source: Broadcom, Nvidia, Intel, Cisco, Marvell.
1Note: Not an exhaustive list; focusing on key partners.​
Why
Tech
What
Market
Where
Sizing
Value Chain
Players
Broadcom: The most comprehensive CPO capability profile

## Slide 26: DeepSeek: Domestic LLM restricted by GPU interconnection bandwidth; CPO as priority exploration direction
Source: Deepseek
CPO: A Crucial Solution
H800 Bandwidth Restricts Training and Inference
H800 Bandwidth Halved Compared to H100
① Network architecture: Forced to use scale-out to compensate for scale-up limitations;
② Training strategy: Tensor parallelism abandoned due to bandwidth constraints;
③ Inference speed: MoE inference rate is 1/20th of H100.
①
②
③
Notes: 1. DS

## Slide 27: DeepSeek: H800, H100, and B200 bandwidth and inference rate comparison
Chart: 
 | 1800 | 900 | 400 | 200
B200
H100
H800
H20
-56%
Inter-card Bandwidth（GB/s）
Source: Deepseek, Nvidia, Huawei
Chart: 
 | 400 | 900
 | 67 | 1200

H800 (DeepSeek)
GB200 NVL72
~18x
Inter-card Bandwidth (GB/s)
Inference Rate (token/s)
① H800 bandwidth halved compared to H100 ;
② If bandwidth returns to the level of B200, the inference rate will increase to ~18 times the original.
Notes: 1. DS

## Slide 28: Overseas strong in electronics, weak in optics; Domestic vise versa - industry evidences
DSP1
7nm-3nm
800G Transceiver1
Packaging/>100nm SiPh
Process Ban
High
Global Market Share
Low
High
Source: Changjiang Securities, Centec Communications IPO Prospectus.
1Data Sources:​​ 800G Transceivers (2025E) | OSAT (2024A) | Switch Chips (2020A) | Electrical DSP Chips (Aug-2023, 50G/100G).
Switch Chip1
16nm-5nm
OSAT1
Limited process ban
Innolight
36%
Eoptolink
23%
Coherent
21%
Mellanox
4%
Accelink&HG
4%
ASE
45%
Amkor
16%
JCET
11%
TFME
8%
Marvell
20%
5nm
Broadcom
62%
5nm
Realtek
16%
Centec
1.6%
16nm
Marvell
65%
3nm
Broadcom
20%
3nm
Credo
<5%
3nm
Domestic
Overseas
Optics
Electronics

## Slide 29: Broadcom CPO industry chain
Source: Broadcom.
Customers
Switch Chip Wafer
EIC Wafer
SiPh Wafer
Switch Chip + CPO
Switch Chip + CPO + Lens
CPO Switch
Laser Chip
ELS Laser Module
Fiber
Design
Foundry
Packaging
Optoelectronic Integration
Final Assembly

## Slide 30: CPO Map
Design House
Foundry
OSAT
Transceiver
Equipment
Operator
eIC
Switch
ASIC
SiPho
Laser